## Slide 1
SECURE STATION DISPATCH
ArUco-Driven AMR Station Identification, HMAC Security & Gazebo Navigation
Amin Ahmed G
B.E. Robotics & Automation Engineering | Anna University
ROS 2 Jazzy | Gazebo Sim (Harmonic) | OpenCV 4.7+

## Slide 2
PROJECT OBJECTIVE
Build a complete AMR dispatch system: a robot tours an industrial facility, reads ArUco markers at 4 stations, authenticates each detection with HMAC-SHA256, and executes station-specific tasks via ROS 2 actions.
Phase 1 -- Dispatch Pipeline
ArUco detection -> state machine -> action-based task execution with JSONL logging
Phase 2 -- Security Hardening
HMAC-SHA256 authentication + pose consistency, with 2 working attack demos
Phase 3 -- Gazebo Simulation
Generated facility, diff-drive AMR, A* planner, stall watchdog, recovery
Tech Stack
ROS 2 Jazzy (Python 3.12)
Gazebo Sim (Harmonic, Ogre2)
OpenCV cv2.aruco (DICT_4X4_50)
HMAC-SHA256 (hashlib)
Custom A* path planner
YAML single source of truth
JSONL event logging

## Slide 3
SYSTEM ARCHITECTURE
marker_detector_node
Camera -> ArUco DICT_4X4_50 -> HMAC sign -> StationMarker
dispatcher_node
IDLE <-> TASK_IN_PROGRESS state machine
verify_hmac() + check_pose() security
Per-marker cooldown, JSONL event logging
task_simulator_node
ROS 2 action server, 5-step tasks with feedback
waypoint_tour_node
A* planner + diff-drive controller + stall watchdog
Reads all geometry from station_registry.yaml
Single Source of Truth
station_registry.yaml owns all geometry.
Everything else reads it or is generated from it:
Gazebo world <- generate_world.py
Navigation <- obstacles_from_registry()
Security <- expected_pose, tolerance
Drift guard <- check_world_sync.py
ROS 2 Topics
/camera/image_raw Gazebo -> detector
/station_marker detector -> dispatcher
/station_task dispatcher -> simulator
/cmd_vel tour -> Gazebo
/odom Gazebo -> tour

## Slide 4
PHASE 1: DISPATCH PIPELINE
StationMarker.msg
marker_id, station_name, robot_pose[7],
confidence, stamp, hmac_signature
StationTask.action
Goal: task_type, station_name
Result: success, summary, execution_time
Feedback: status, progress
State Machine
IDLE -> marker arrives -> TASK_IN_PROGRESS
Action result -> log to JSONL -> IDLE
Station Registry
ID 0 Inspection [1.0, 2.0] ~3.0s
ID 1 Assembly [4.5, 1.0] ~3.5s
ID 2 Storage [4.5, 5.0] ~2.7s
ID 3 Charging [0.5, 5.5] ~3.5s
Pipeline Test: 4/4 PASS
8 events logged (4 DISPATCHED + 4 COMPLETED)
All markers detected and tasks executed

## Slide 5
PHASE 2: HMAC SECURITY
Threat Model
A forged ROS message or printed marker could
drive a facility robot anywhere.
Mitigation 1: HMAC-SHA256
Detector signs each detection with per-station
pre-shared key. Dispatcher verifies signature.
Invalid/missing -> AUTH_FAIL
Mitigation 2: Pose Consistency
check_pose() compares robot_pose against
expected_pose within tolerance (0.5 m).
Too far -> LOCATION_MISMATCH
Attack Demonstrations
spoof_marker_publish.py
Publishes forged StationMarker with invalid
HMAC -> dispatcher rejects -> AUTH_FAIL
location_mismatch_attack.py
Valid HMAC but pose [99, 99, 0] ->
HMAC passes, pose fails -> LOCATION_MISMATCH
Security Test: 3/3 PASS
Valid marker dispatched + completed
Spoofed HMAC rejected
Location mismatch rejected

## Slide 6
PHASE 3: GAZEBO SIMULATION & NAVIGATION
Generated Facility
8.5m x 9.5m walled enclosure
4 perimeter bays with ArUco sign stacks
World SDF generated from station_registry.yaml
AMR Robot
0.40m x 0.30m diff-drive chassis
0.85m sensor mast with front camera
Camera height = marker board height
Navigation Stack (ROS-free)
planner.py: A* visibility-graph, 2 clearance layers
controller.py: turn-then-arc, proportional decel
StallWatchdog: <4cm in 3s -> reverse + replan
perception_budget.py: range gate via confidence
Perception Budget
confidence = min(perimeter_px / 1200, 1.0)
1.50m (berth): 259px, 0.86 ACCEPT
1.72m (gate): 226px, 0.75 ACCEPT
1.90m: 204px, 0.68 REJECT
Board legible only from its own berth.
Navigation Test: 23/23 PASS
17/17 planner + perception regressions
6/6 offline tour simulation
0 obstacle contacts, 0.528m min clearance

## Slide 7
FULL TOUR RESULTS
Station Arrival Log (Gazebo /odom)
Station | Target Coords | Arrived Pose | Error | Status
Inspection | [1.00, 2.00] | [0.95, 2.21] | 0.219 m | DISPATCHED -> COMPLETED
Assembly | [4.50, 1.00] | [4.31, 1.10] | 0.217 m | DISPATCHED -> COMPLETED
Storage | [4.50, 5.00] | [4.49, 4.78] | 0.217 m | DISPATCHED -> COMPLETED
Charging | [0.50, 5.50] | [0.72, 5.48] | 0.219 m | DISPATCHED -> COMPLETED
All 4 stations visited, all tasks DISPATCHED and COMPLETED. 5 test suites: from 1-second ROS-free regression to full 2-minute Gazebo demo.

## Slide 8
CHALLENGES & LESSONS
1. CMake Target Collision
rosidl + ament_python_install_package() conflict.
Fix: install(DIRECTORY) into site-packages.
2. Open-Loop False Successes
Robot drove straight, logs showed 4/4 PASS.
Fix: closed-loop P-controller using /odom.
3. Marker Panel Collision (4 defects)
Robot wedged into Assembly panel, reported success.
Layout: panels in driving path
Planning: no obstacle awareness
Control: no stall detection
Reporting: timeout = success
Fix: single source of truth, A* planner,
stall watchdog, honest reporting.
4. Signage Collision Geometry
Decorative posts too close to stopping pose.
Fix: ultra-thin collision (0.01m depth).

## Slide 9
CONCLUSION
Complete, tested AMR dispatch system delivered:
Phase 1: Working perception -> dispatch -> execution pipeline with custom ROS 2 interfaces, FSM, and JSONL event logging.
Phase 2: HMAC-SHA256 auth + pose consistency reject forged/replayed messages. Two attack scripts demonstrate both rejection paths.
Phase 3: Obstacle-aware A* navigation in generated Gazebo facility with stall watchdog, closed-loop control, and automatic recovery.
Single source of truth (station_registry.yaml) eliminates geometry disagreements between simulator, planner, and security.
5 test suites verify every layer independently.
github.com/Amin-Ahmed-G/secure_station_dispatch